## Slide 1: Introducing the River Basin Export Reduction Optimization Support Tool (RBEROST)
1 ORISE – EPA, ORD/CEMM, Atlantic Coastal Environmental Sciences Division, Narragansett, RI
2 ORD/CEMM, Atlantic Coastal Environmental Sciences Division, EPA, Narragansett, RI
1
USEPA R User Group Workshop 2021
Catherine Chamberlin1, Marilyn ten Brink2, Naomi Detenbeck2

## Slide 2: Outline:
2
Purpose and goals of the River Basin Export Reduction Optimization Support Tool (RBEROST)
Mathematical optimization
Software structure of the tool
Using R and Shiny for a clean user interface
Lessons learned
Future directions

## Slide 3: Problem:
3
Purpose and goals of the River Basin Export Reduction Optimization Support Tool (RBEROST)

## Slide 4: Goal:
4
Develop and a regional optimization tool to allow stakeholders to find the least-cost solution to meet nutrient loading targets
Purpose and goals of the River Basin Export Reduction Optimization Support Tool (RBEROST)

## Slide 5: Illustrative Case Study:
5
Photo Credit: The Long Island Sound Study
The tool developed for this case study needs to be extensible to a larger region
  Tool should be built on national and regional datasets
Purpose and goals of the River Basin Export Reduction Optimization Support Tool (RBEROST)

## Slide 6: Necessary tool properties:
6
Photo Credit: The Long Island Sound Study
The tool developed for this case study needs to be extensible to a larger region
  Tool should be built on national and regional datasets
~ 16,000 km2;
  need a tool that can optimize large spatial scales without extensive computational resources
Purpose and goals of the River Basin Export Reduction Optimization Support Tool (RBEROST)

## Slide 7: Necessary tool properties:
7
The tool developed for this case study needs to be extensible to a larger region
  Tool should be built on national and regional datasets
~ 16,000 km2;
  Tool should be able to optimize large spatial scales without extensive computational resources
Both Total Nitrogen and Total Phosphorus contribute to water quality issues
  Tool should be able to optimize for loads of multiple constituents at one.
Purpose and goals of the River Basin Export Reduction Optimization Support Tool (RBEROST)

## Slide 8
8
Photo Credit: eutrophication&hypoxia (Flickr)
Photo Credit: Iowa Agriculture Water Alliance
Photo Credit: DASonnenfeld (Wikimedia)
Photo Credit: Tony Webster (Flickr)
Necessary tool properties:
The tool developed for this case study needs to be extensible to a larger region
  Tool should be built on national and regional datasets
~ 16,000 km2;
  Tool should be able to optimize large spatial scales without extensive computational resources
Both Total Nitrogen and Total Phosphorus contribute to water quality issues
  Tool should be able to optimize for loads of multiple constituents at one.
Treatments exist for diverse point and non-point sources
  Tool should consider treatments for nutrients from both point and non-point sources from a variety of land use types.
Purpose and goals of the River Basin Export Reduction Optimization Support Tool (RBEROST)

## Slide 9
9
Necessary tool properties:
The tool developed for this case study needs to be extensible to a larger region
  Tool should be built on national and regional datasets
~ 16,000 km2;
  Tool should be able to optimize large spatial scales without extensive computational resources
Both Total Nitrogen and Total Phosphorus contribute to water quality issues
  Tool should be able to optimize for loads of multiple constituents at one.
Treatments exist for diverse point and non-point sources
  Tool should consider treatments for nutrients from both point and non-point sources from a variety of land use types.
Potential tool users have a wide variety of backgrounds and experiences.
  Tool should not require knowledge or expertise in code and should have a user-friendly interaction.
Purpose and goals of the River Basin Export Reduction Optimization Support Tool (RBEROST)

## Slide 10: Mathematical Optimization:
All loading targets must be met:
  n is the number of catchments in the watershed
  BMP is “Best Management Practice”, or the specific practice implemented
  WWTP is “wastewater treatment plant”
Optimize the least-cost solution
10
Mathematical Optimization

## Slide 11: Optimization in A Mathematical Programming Language (AMPL):
11
Legend:
Data
Optimization Support File
User Input/Interaction
Result
Model
Optimization Solver (CPLEX)
AMPL Model File
AMPL Data File
AMPL Command File
Best Management Practice (BMP) selection at minimized cost
Software structure of the tool
Linear mixed-integer optimization
Make use of free community solvers hosted on a web server

## Slide 12: Data and user-specifications are input as csv files
12
Using R and Shiny for a clean user interface

## Slide 13: Data inputs are varied:
13
& many many others
Software structure of the tool

## Slide 14: Use R to write AMPL:
14
Legend:
Data
Optimization Support File
User Input/Interaction
Result
Model
Optimization Solver
AMPL Model File
AMPL Data File
AMPL Command File
Best Management Practice (BMP) selection at minimized cost
Preprocessor
User specified BMP specs (csv)
User specified loading targets (csv)
Nutrient Removal Efficiency Data
2012 Regional SPARROW model
Landcover Data
Cost Data
Software structure of the tool

## Slide 15: Use R and Shiny to view results and generate output data:
Software structure of the tool
15
Legend:
Data
Optimization Support File
User Input/Interaction
Result
Model
Postprocessor
Summary Report
CSV files of BMP implementation in each catchment
Optimization Solver
AMPL Model File
AMPL Data File
AMPL Command File
Best Management Practice (BMP) selection at minimized cost
Preprocessor
User specified BMP specs (csv)
User specified loading targets (csv)
Nutrient Removal Efficiency Data
2012 Regional SPARROW model
Landcover Data
Cost Data

## Slide 16: Tool distribution
16
www.GitHub.com/USEPA/RBEROST
Software structure of the tool

## Slide 17: All* steps of the tool are presented to the user with minimal code interaction:
17
Using R and Shiny for a clean user interface
RMarkdown file with 3 code chunks
  configureR (installs all necessary packages)
  runpreprocessor (takes a few user inputs and sources necessary code to write the AMPL files)
  runpostprocessor (launches the Shiny app to view results)
* Interaction with the server still requires users to navigate web submission forms on their own

## Slide 18: Shiny postprocessor:
18
Using R and Shiny for a clean user interface

## Slide 19
19
Shiny postprocessor:
Using R and Shiny for a clean user interface

## Slide 20
20
Shiny postprocessor:
Using R and Shiny for a clean user interface

## Slide 21
21
Shiny postprocessor:
Using R and Shiny for a clean user interface

## Slide 22: Lessons Learned:
22
Lessons Learned
Debugging Shiny != debugging R
  Frequent use of browser() function for debugging
  Printing out basic interactive statistics to the R console (not the Shiny window) can be immensely helpful for tracking reactivity
Sourcing User Interface files/functions is an easy way to maintain Shiny app organization
  Sourcing server functions is less straight forward – must move the bulk of code to functions and source the functions that are then called within reactive code sections
Basic functions (e.g. read.csv()) may behave differently in different versions of R.
  Code needs to be tested on multiple versions of R to be robust.
Code distribution mechanism matters!
  Consider how code will be distributed as soon as possible in the planning process.
  There are likely many workable in-betweens if the ideal delivery mechanism has challenges.

## Slide 23: Future Directions:
23
Work the preprocessing step and the online server interaction into the Shiny app to further reduce interaction with source code.
Made data available for users online and provide an option to source this data through the tool. This reduces interaction with many csv files.
Expand the geographic range of available data to the entire northeast. Current version of RBEROST can be used anywhere within the northeast domain of the USGS regional SPARROW model.
Providing flexibility for RBEROST to be used in the Pacific regional SPARROW model area as well.
Future Directions

## Slide 24: Thanks for Listening!
24
Emails:
chamberlin.catherine@epa.gov
Detenbeck.Naomi@epa.gov